Safe Insecure Wireless Surfing
Or How To SSH Home And Proxy The Web
Presented By
Chuck Frain

---
What This Talk Is (And Isn't)
- Is: Overview Of Securely Connecting Home Over Insecure Networks
- Is: What Software Needs To Be Installed and Configured
- Isn't: Detailed Instructions On Configuring Said Software

---
What's Needed At Home
- Router
  - Know Your IP Or Use A Dynamic DNS Address
    - Such as provided by dyndns.org
  - Port Forward Or DMZ To Server
- Server
  - Sshd Server That Allows Port Forwarding
  - Squid Proxy Server Properly Configured
    - I Suggest A Username And Password
  - Fwknop Server (optional)

---
What's Needed At Hotel
- PC Or Device With SSH Client That Handles Port Forwarding
- Software That Can Use A Proxy Server For Connections
- A Good Firewall On Your Device
  - Better yet, No Open Ports At All
- Fwknop client (if on server)

---
What You Need To Do
- From The PC Establish A SSH PortForward Connection
- Command Line Example
  ssh -L 1492:localhost:3128 172.20.20.51 -p 22
- SSH Config Example
  Host homevpn1
  Hostname 172.20.20.51
  LocalForward 1492 localhost:3128

---
Configure Your Software
- Firefox
  - FoxyProxy Add-On
- Individual Software Packages Configured
- OS
  - Set Global Option

---
Connect Home And Surf
Enjoy your ssh protected proxy connection to your home network and resources.